## Slide 1
MPLS route management
Leone Giuseppe, 10518770
Petocchi Alessandro, 10661410
Sodano Marco, 10495166
Villa Veronica, 10503254
Switching and Routing project 2018/2019
Prof. Guido Maier
Ph.D. student Sebastian Troìa

## Slide 2: Outline
Introduction
…
…
…

## Slide 3: Introduction
Starting from a multipath network with multiple disjoint paths from a source and a destination, a Ryu application has been implemented to set up a pair of MPLS link‐disjoint tunnels to connect the source with the destination.
One tunnel is the default path, the other is the back‐up path.
MPLS connection is based on source and destination MACs
The application is able to re‐route traffic on the back‐up path in case of a failure of a link of the default path and to restore the original ruleset when the default path returns to a working state.

## Slide 4: MPLS connection setup
host1
host2
h1 wants to establish an IP connection with h2
All the flow tables of the switches inside the network are empty (only default rule is installed)
When the firtst IP packet comes to the switch connected to h1, the controller installs MPLS rules in the switches of default and backup paths
CONTROLLER

## Slide 5: Packet in handler
Once topology and border switches are known, the controller computes a list of paths without links in common sorted by increasing number of edges
The first one is selected as default path assigning a label value chosen randomly
The second element is the backup path with label equal to default one increased by a unit
If the list contains just one element, only the default path is avaliable

## Slide 6: Rule installation
The controller installs MPLS PUSH rule in the in order to add labels on packets in the node directly connected to the host
Intermediate nodes contain just forwarding rules based on label matching
In the last node POP MPLS rule is installed in order to remove label from the packet and deliver it to the host
At the same time symmetrical rules are placed to allow packets to come back on the same path
Intermediate switches are able to recognize the direction of the packets checking the input port
The same procedure is applied to backup path, but rules have a lower priority the default ones

## Slide 7: Path configuration example
Default path Backup path
Action set for switch 1: PUSH MPLS (label=1) outport 2, priority 2 (default)
PUSH MPLS (label=2) outport 3, priority 1 (backup)
POP MPLS (label=1) outport 1, priority 2 (default) POP MPLS (label=2) outport 1, priority 1 (backup)
Action set for switch 2: PUSH MPLS (label=1) outport 2, priority 2 (default)
PUSH MPLS (label=2) outport 3, priority 1 (backup)
POP MPLS (label=1) outport 1, priority 2 (default) POP MPLS (label=2) outport 1, priority 1 (backup)
Action set on switch 3:
Inport 1 (label=1) => outport 2
Inport 2 (label=1) => outport 1
Action set on switch 4:
Inport 1 (label=2) => outport 2
Inport 2 (label=2) => outport 1
Notes: Host 1 host 2

## Slide 8: Link down
When link goes down, the controller detects which MPLS connection were using that link and deletes corresponding rules
Packets will be automatically routed on backup path
Action set for switch 1:
PUSH MPLS (label=2) outport 3, priority 1 (backup) POP MPLS (label=2) outport 1, priority 1 (backup)
Action set for switch 2:
PUSH MPLS (label=2) outport 3, priority 1 (backup) POP MPLS (label=2) outport 1, priority 1 (backup)
Action set on switch 4:
Inport 1 (label=2) => outport 2
Inport 2 (label=2) => outport 1

## Slide 9: Link up
When the link returns active, all of the dafault rules are re-installed and packets will be routed again on the previous path

## Slide 10: Port detection

## Slide 11: Exception management
Notes: Se va giu quello di bu, port detect

## Slide 12
END
Questions?