## Slide 1
MPLS route management
Leone Giuseppe, 10518770
Petocchi Alessandro, 10661410
Sodano Marco, 10495166
Villa Veronica, 10503254
Switching and Routing project 2018/2019
Prof. Guido Maier
Tutor. Sebastian Troìa

## Slide 2: Outline
Introduction
Flow chart of the algorithm
Mininet example
Differences testbed-mininet simulator
Statistics

## Slide 3: Introduction
GOAL
The goal is to implement a Ryu application to set up a pair of MPLS link‐disjoint tunnels to connect two hosts in a network.
ASSUMPTIONS
  The MPLS connection is based on source and destination MACs
  The application is able to re‐route traffic on the back‐up path in case of a failure of a link of the default path
The project works both on mininet and the testbed

## Slide 4: Objective of the project
host1
host2
host1 wants to establish an IP connection with host2
All the flow tables of the switches inside the network are empty (only table-miss rules are installed)
CONTROLLER

## Slide 5
Yes
add hash (srcMAC,dstMAC) in the list
Compute the path_list (edge_disjoint_paths)
between source and destination
No
Flow chart of the algorithm(1)

## Slide 6
Flow chart of the algorithm(2)

## Slide 7: Path configuration example (mininet)
Default path Backup path
Action set for switch 1: PUSH MPLS (label=1) out port 2, priority 2 (default)
PUSH MPLS (label=2) out port 3, priority 1 (backup)
POP MPLS (label=1) out port 1, priority 2 (default) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set for switch 2: PUSH MPLS (label=1) out port 2, priority 2 (default)
PUSH MPLS (label=2) out port 3, priority 1 (backup)
POP MPLS (label=1) out port 1, priority 2 (default) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set on switch 3:
In port 1 (label=1) => out port 2
In port 2 (label=1) => out port 1
Action set on switch 4:
In port 1 (label=2) => out port 2
In port 2 (label=2) => out port 1
CONTROLLER
IP PACKET
IP PACKET
IP PACKET
The next packets will be
forwarded directly by the switches, since the new rules are installed
Notes: Parlare qui delle diverse priorità dei path

## Slide 8: Port detection
When a link goes up/down, the port status of the switches involved in the connection will change consequently
The switches notify the event to the controller with port status messages

## Slide 9: Link down/up (mininet)
Default path Backup path
Action set for switch 1: PUSH MPLS (label=1) out port 2, priority 2 (default)
PUSH MPLS (label=2) out port 3, priority 1 (backup)
POP MPLS (label=1) out port 1, priority 2 (default) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set for switch 2: PUSH MPLS (label=1) out port 2, priority 2 (default)
PUSH MPLS (label=2) out port 3, priority 1 (backup)
POP MPLS (label=1) out port 1, priority 2 (default) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set on switch 3:
In port 1 (label=1) => out port 2
In port 2 (label=1) => out port 1
Action set on switch 4:
In port 1 (label=2) => out port 2
In port 2 (label=2) => out port 1
CONTROLLER
IP PACT
Notes: Parlare qui delle diverse priorità dei path

## Slide 10: Differences mininet simulator-testbed
MININET SIM. | TESTBED
Open vSwitch switches | Zodiac FX switches
Access directly to the host | Access to RaspPi via SSH
ARP tables always filled | ARP tables may be empty
Matching on MPLS label | Doesn’t match on label field
Topology is completely reliable | Topology is instable
Virtual topology | Real topology with physical links among switches
No broadcast IP msg. | Switches periodically send broadcast IP msg.
No specific event is triggered when a port becomes active | Switches notify with an OFPPS_LIVE event when a port becomes active
Notes: Testbed matching: ETH_TYPE_MPLS, src_MAC, dst_MAC, in_port (in intermediate switches, label still present)
Topology instable= store 2 network, one updated to compute edge disjoint and another for getting info about ports, detapath…
OFPPS_LIVE triggered when a port is active

## Slide 11: Statistics collection: experiment procedure
Run the controller and then activate the topology
Verify whether ARP tables are full
Establish an IP connection between 2 hosts
Once MPLS rules have been installed, collect statistics about RULE INSTALLATION TIME
Simulate a link failure
Collect statistics about PATH MODIFICATION TIME
Restore the link
Collect statistics about PATH MODIFICATION TIME
Notes: For both mininet7testbed

## Slide 12: Testbed statistics vs mininet: rules installation time
Chart: Rules installation time - MININET SIMULATOR
 | 0.006803 | 0.007372 | 0.007373 | 0.007374 | 0.007375 | 0.007376 | 0.007377 | 0.007378 | 0.007379 | 0.00738
 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187
Chart: Rules installation time - TESTBED
 | 0.27818 | 0.004499 | 0.088249 | 0.44452 | 0.33728 | 0.001817 | 1.0886 | 0.30132
Average+Foglio1!$B$1:$B$8 | 0.31806 | 0.31806 | 0.31806 | 0.31806 | 0.31806 | 0.31806 | 0.31806 | 0.31806
In case of empty ARP table, rule installation takes several seconds
Notes: Rule installation delayed by arp procedure

## Slide 13: Testbed statistics vs mininet: path modification time
Chart: Path modification time - TESTBED
 | 0.32311 | 0.005377 | 0.16967 | 0.00317 | 0.00469 | 0.080493 | 0.002706 | 0.23217 | 0.004827 | 0.003831
 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004
Chart: Path modification time - MININET SIMULATION
 | 0.003742 | 0.00788 | 0.003256 | 0.00376 | 0.003453 | 0.003907 | 0.003042 | 0.003474 | 0.003638 | 0.004768
 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092
Notes: Plug followed by unplug…?

## Slide 14: Testbed statistics: packet loss during path change
Chart: Time
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Default Path
Back-up Path
∆t=0.08s
Bandwidth | 10 kbit/s | 100 kbit/s | 1 Mbit/s | 10 Mbit/s
Mininet | 0.19% | 0.27% | 0.50% | 1,71%
Testbed | 0,42% | 0,78% | 1,39% | 3,28%
Packet loss (%)
Transitions between paths generate packet losses. The tests were performed with iperf (UDP): the results in the table are an average over multiple experiments.

## Slide 15
END