## Slide 1
MPLS route management
Leone Giuseppe, 10518770
Petocchi Alessandro, 10661410
Sodano Marco, 10495166
Villa Veronica, 10503254
Switching and Routing project 2018/2019
Prof. Guido Maier
Ph.D. student Sebastian Troìa

## Slide 2: Outline
Introduction
MPLS connection setup
Packet in handler
Rule installation
Port detection
Link down/up
Differences testbed-mininet simulator
Statistics

## Slide 3: Introduction
Starting from a multipath network with multiple disjoint paths from a source and a destination, a Ryu application has been implemented to set up a pair of MPLS link‐disjoint tunnels to connect the source with the destination.
One tunnel is the default path, the other is the back‐up path.
MPLS connection is based on source and destination MACs
The application is able to re‐route traffic on the back‐up path in case of a failure of a link of the default path and to restore the original ruleset when the default path returns to a working state.

## Slide 4: MPLS connection setup
host1
host2
h1 wants to establish an IP connection with h2
All the flow tables of the switches inside the network are empty (only the default rule is installed)
CONTROLLER

## Slide 5: Packet in handler
add hash (srcMAC,dstMAC) in the list
Yes
No

## Slide 6: Rule installation

## Slide 7: Path configuration example
Default path Backup path
Action set for switch 1: PUSH MPLS (label=1) out port 2, priority 2 (default)
PUSH MPLS (label=2) out port 3, priority 1 (backup)
POP MPLS (label=1) out port 1, priority 2 (default) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set for switch 2: PUSH MPLS (label=1) out port 2, priority 2 (default)
PUSH MPLS (label=2) out port 3, priority 1 (backup)
POP MPLS (label=1) out port 1, priority 2 (default) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set on switch 3:
In port 1 (label=1) => out port 2
In port 2 (label=1) => out port 1
Action set on switch 4:
In port 1 (label=2) => out port 2
In port 2 (label=2) => out port 1
Notes: Parlare qui delle diverse priorità dei path

## Slide 8: Port detection
When a link goes up/down, the port status of the switches involved in the connection will change consequently
The switches notify the event to the controller with port status messages

## Slide 9: Link down
When a link goes down, the controller detects it and deletes the corresponding rules
Packets will be automatically routed on the backup path
Action set for switch 1:
PUSH MPLS (label=2) out port 3, priority 1 (backup) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set for switch 2:
PUSH MPLS (label=2) out port 3, priority 1 (backup) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set on switch 4:
In port 1 (label=2) => out port 2
In port 2 (label=2) => out port 1

## Slide 10: Link up
When the link returns active, all of the default rules are re-installed and packets will be routed again on the previous path (higher priority)

## Slide 11: Differences testbed-mininet simulator
In the testbed version of the code, MPLS rules don’t match on label field

## Slide 12: Statistics: rules installation time
Chart: Rules installation time - TESTBED
 | 3.9634 | 0.27818 | 5.5987 | 0.004499 | 0.088249 | 0.44452 | 0.33728 | 0.001817 | 1.0886 | 0.30132
Chart: Rules installation time - MININET SIMULATOR
 | 0.006803 | 0.007372 | 0.007373 | 0.007374 | 0.007375 | 0.007376 | 0.007377 | 0.007378 | 0.007379 | 0.00738

## Slide 13: Statistics: path modification time
Chart: Path modification time - MININET SIMULATOR
 | 0.003742 | 0.00788 | 0.003256 | 0.00376 | 0.003453 | 0.003907 | 0.003042 | 0.003474 | 0.003638 | 0.004768
Chart: Path modification time - TESTBED
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
 | 0.32311 | 0.005377 | 0.16967 | 0.00317 | 0.00469 | 0.080493 | 0.002706 | 0.23217 | 0.004827 | 0.003831

## Slide 14: Statistics: packets status
Chart: SPEED (KBIT/S)
| 1 | 100 | 1000 | 10000
Mininet Simulator | 0 | 0 | 0 | 0
Testbed | 0 | 0 | 1.3 | 2.1
Notes: Solo un grafico con bw/pkt loss per testbed e mininet

## Slide 15
END
Do you have any questions?