## Slide 1
MPLS route management
Leone Giuseppe, 10518770
Petocchi Alessandro, 10661410
Sodano Marco, 10495166
Villa Veronica, 10503254
Switching and Routing project 2018/2019
Prof. Guido Maier
Tutor. Sebastian Troìa

## Slide 2: Outline
Introduction
Flow chart of the algorithm
Mininet example
Differences testbed-mininet simulator
Statistics

## Slide 3: Introduction
Implement a Ryu application to set up a pair of MPLS link‐disjoint tunnels to connect the source with the destination.
MPLS connection is based on source and destination MACs
The application is able to re‐route traffic on the back‐up path in case of a failure of a link of the default path
Project has been developed both on mininet and testbed

## Slide 4: Objective of the project
host1
host2
host1 wants to establish an TCP connection with host2
All the flow tables of the switches inside the network are empty (only the default rule is installed)
CONTROLLER

## Slide 5
Yes
add hash (srcMAC,dstMAC) in the list
Compute path_list=edge_disjoint_paths
between switchSRC and
switchDST
No
Flow chart of the algorithm(1)

## Slide 6
Flow chart of the algorithm(2)

## Slide 7: Path configuration example (mininet)
Default path Backup path
Action set for switch 1: PUSH MPLS (label=1) out port 2, priority 2 (default)
PUSH MPLS (label=2) out port 3, priority 1 (backup)
POP MPLS (label=1) out port 1, priority 2 (default) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set for switch 2: PUSH MPLS (label=1) out port 2, priority 2 (default)
PUSH MPLS (label=2) out port 3, priority 1 (backup)
POP MPLS (label=1) out port 1, priority 2 (default) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set on switch 3:
In port 1 (label=1) => out port 2
In port 2 (label=1) => out port 1
Action set on switch 4:
In port 1 (label=2) => out port 2
In port 2 (label=2) => out port 1
CONTROLLER
IP PACKET
IP PACKET
IP PACKET
The next packets will be
forwarded directly by the switches, since the new rules are installed
Notes: Parlare qui delle diverse priorità dei path

## Slide 8: Port detection
When a link goes up/down, the port status of the switches involved in the connection will change consequently
The switches notify the event to the controller with port status messages

## Slide 9: Link down/up (mininet)
Default path Backup path
Action set for switch 1: PUSH MPLS (label=1) out port 2, priority 2 (default)
PUSH MPLS (label=2) out port 3, priority 1 (backup)
POP MPLS (label=1) out port 1, priority 2 (default) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set for switch 2: PUSH MPLS (label=1) out port 2, priority 2 (default)
PUSH MPLS (label=2) out port 3, priority 1 (backup)
POP MPLS (label=1) out port 1, priority 2 (default) POP MPLS (label=2) out port 1, priority 1 (backup)
Action set on switch 3:
In port 1 (label=1) => out port 2
In port 2 (label=1) => out port 1
Action set on switch 4:
In port 1 (label=2) => out port 2
In port 2 (label=2) => out port 1
CONTROLLER
IP PACT
Notes: Parlare qui delle diverse priorità dei path

## Slide 10: Differences mininet simulator-testbed
MININET SIM. | TESTBED
Open vSwitch switches | Zodiac FX switches
Access directly to the host | Access to RaspPi via SSH
ARP tables always filled | ARP tables may be empty
Matching on MPLS label | Doesn’t match on label field
Topology is completely reliable | Topology is instable
Virtual topology | Real topology with physical links among switches
No broadcast IP msg. | Switches periodically send broadcast IP msg.
No specific event is triggered when a port becomes active | Switches notify with an OFPPS_LIVE event when a port becomes active
Notes: Testbed matching: ETH_TYPE_MPLS, src_MAC, dst_MAC, in_port (in intermediate switches, label still present)
Topology instable= store 2 network, one updated to compute edge disjoint and another for getting info about ports, detapath…
OFPPS_LIVE triggered when a port is active

## Slide 11: Statistics collection: experiment procedure
Run the controller and then activate the topology
Verify whether ARP tables are full
Establish an IP connection between 2 hosts
Once MPLS rules have been installed, collect statistics about RULE INSTALLATION TIME
Simulate a link failure
Collect statistics about PATH MODIFICATION TIME
Restore the link
Collect statistics about PATH MODIFICATION TIME
Notes: For both mininet7testbed

## Slide 12: Testbed statistics vs mininet: rules installation time
Chart: Rules installation time - MININET SIMULATOR
 | 0.006803 | 0.007372 | 0.007373 | 0.007374 | 0.007375 | 0.007376 | 0.007377 | 0.007378 | 0.007379 | 0.00738
 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187 | 0.0073187
Chart: Rules installation time - TESTBED
 | 0.27818 | 0.004499 | 0.088249 | 0.44452 | 0.33728 | 0.001817 | 1.0886 | 0.30132
Average+Foglio1!$B$1:$B$8 | 0.31806 | 0.31806 | 0.31806 | 0.31806 | 0.31806 | 0.31806 | 0.31806 | 0.31806
In case of empty ARP table, rule installation takes several seconds
Notes: Rule installation delayed by arp procedure

## Slide 13: Testbed statistics vs mininet: path modification time
Chart: Path modification time - TESTBED
 | 0.32311 | 0.005377 | 0.16967 | 0.00317 | 0.00469 | 0.080493 | 0.002706 | 0.23217 | 0.004827 | 0.003831
 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004 | 0.083004
Chart: Path modification time - MININET SIMULATION
 | 0.003742 | 0.00788 | 0.003256 | 0.00376 | 0.003453 | 0.003907 | 0.003042 | 0.003474 | 0.003638 | 0.004768
 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092 | 0.004092
Notes: Plug followed by unplug…?

## Slide 14: Testbed statistics: packet loss during switching events
Chart: SPEED (KBIT/S)
| 1 | 100 | 1000 | 10000
Mininet Simulator | 0 | 0 | 0 | 0
Testbed | 0 | 0 | 1.3 | 2.1
Notes: Solo un grafico con bw/pkt loss per testbed e mininet

## Slide 15
Chart: Time(s)
| 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Default Path
Back-up Path

## Slide 16
END